## Slide 1: Long-range IoT technologies: the dawn of LoRaTM
Lorenzo Vangelista
Michele Zorzi
Andrea Zanella
FABULOUS 23-25 Sep. 2015, Ohrid, Rep. of Macedonia
SIGnals processing & NETworking research group
SIGNET

## Slide 2: IoT Service Requirements
Place-&-Play
Ubiquitous coverage
Low Cost
Simple Hardware
Massive production
Zero-configuration
Little maintenance
Very long battery life
Very low fault rate
Digital Divide*
Educate people in using the technologies
Providing basic Internet access for free
* Credits to the inspiring talk by Josef Noil

## Slide 3: Three main approaches
Short-range multihop
  ZigBee
  WiFi low energy
  RFID
Cellular
  GSM
  LTE-A
  5G
Internet
NetServer
LPWAN gateway
LPWAN gateway
Low Power Wide Area Networks (LPWAN)
  SIGFOX
  Neul
  LoRa

## Slide 4: Quick comparison
Range
Power
consumption
Bitrate
Radio chipset
costs
Service subscription costs
Number of
Base Stations/collectors
Transmission
latency
Geographical
coverage, penetration
LPWAN
cellular
Shortrange
multihop

## Slide 5: LPWAN: general profile
ISM Frequency Bands
  In Europe: Short Range Device 860 MHz: 863-870 MHz
  “Short Range” is misleading  regulations constraints are on transmit power and channel occupancy only
Two main solutions
  UNB: Ultra Narrow Band
    Bandwidth in the order of 25 kHz;
  WB: Wideband (spread spectrum)
    Bandwidth from 125 kHz to 250 kHz

## Slide 6
Origin:
  Founded in 2009, and growing very fast since then
  First LPWAN technology proposed in the IoT market
  $115 million from investors as Telefonica and Vodafone
Secret sauce: proprietary network layer protocols
  UNB modulation, SDR860 band (Europe)
Coverage:
  30-50 km in rural areas and 3-10 km in urban areas

## Slide 7: SIGFOX coverage
Source: http://www.sigfox.com/en/#!/connected-world/sigfox-network-operator

## Slide 8
Origin:
  Open standard backed by Neul
  Acquired by Huawei in 2014 for $25 millions
Secret sauce: multiple flavours
  Star topology, UNB, sub-GHz or TV white space
 | Wightless-N | Wightless-P | Wightless-W
Directionality | 1-way | 2-way | 2-way
Feature set | Simple | Full | Extensive
Range | 5km+ | 2km+ | 5km+
Battery life | 10 years | 3-8 years | 2-5 years
Terminal cost | Very low | Low | Low-medium
Network cost | Very low | Low | Low-medium
Notes:   Weightless-N
    star network architecture in sub-GHz
    UNB technology,
    excellent range of several kilometres even urban
  Weightless-P
    narrowband channels of 12.5 kHz, with FDMA&TDMA
    adaptive data rate from 0.2 kbit/s to 100 kbit/s
    time-synchronised aggregators
  Weightless-W
    star topology operating in TV white space spectrum

## Slide 9
Origin:
  Started in San Diego (USA) as On-Ramp Wireless
  Started with smart metering
  Pioneering the 802.15.4k standard
  Raised at least $67 million to date, mainly from energy and electric utility companies
Secret sauce:
  Random Phase Multiple Access (RPMA) – patented
  Work on ISM 2.4 GHz with very low receiver sensitivity
  Apply power control, adaptive spreading, multipacket reception, …
Capacity & Coverage
  ~19kbit/MHz over up to 10 km in EU, 30 km in USA

## Slide 10: SEMTECH LoRA
Img source: http://wataridori.megamistudios.com/2015/04/the-dawn-to-end-all-nights-thats-what-we-thought-it-was/

## Slide 11
Origin:
  First proposed by SemTech (France)
  Now being developed by the LoRa Alliance
    https://www.lora-alliance.org
    Cisco, IBM, SemTech, …
Secret sauce:
  Wideband CIRP-like PHY layer with adaptive rate
  Simple but effective LoRA WAN MAC protocol
Capacity & Coverage
  From order of 102 to 104 bit/s over up to 1-3 km in EU

## Slide 12: LoRaTM system architecture
LoRA
End Device
LoRA
End Device
LoRA
End Device
LoRA
End Device
LoRA
GW
LoRA
End Device
LoRA
End Device
LoRA
End Device
LoRA
End Device
LoRA
GW
LoRa Network Server
INTERNET
IP connections
LoRa links
LoRa links
LoRA
End Device

## Slide 13: LoRa Class A
Class A (all)
Mandatory supported by all LoRa devices
End-devices start packet exchange with uplink tx followed by two receive windows
Adaptive modulation
Very low energy consumption
Suitable for monitoring services, with mostly uplink traffic

## Slide 14: LoRa Class B
Class B (beacon)
Time synchronization using beacons sent by gateways  receive window opens in planned periodic intervals
Low energy consumption (especially for asynchronous bidirectional communications)
Suitable for switches/actuators controlled by NetServer
  Command latency in the order of seconds

## Slide 15: LoRa Class C
Class C (continuously listening)
End devices are always ready to receive signals from the gateways (except when transmitting)
Medium/High energy consumption at end device
Suitable for actuations with strict time constraints
  Automation, control, etc…

## Slide 16: PHY frame and bitrates
6 channels of 125 kHz + 1 channel of 250 kHz (EU)
7 different spreading factors  bitrates from 0.3 kbit/s to ~11 kbit/s
Gateways can receive multiple signals simultaneously
  Because of the orthogonality of spreading sequences
Source: SX1272/3/6/7/8: LoRa Modem Designer’s Guide AN1200.13

## Slide 17: Wrapping up
Wideband chirp modulation allows for long-range, robust communications, with low complexity, low power and low cost receivers
Can use common upper layer protocols
  e.g., the security mechanisms already tested in IEEE 802.15.4 networks
LoRa Alliance is boosting LoRa technology, marketing, strategy, and interoperability aspects  development of a strong eco-system around the technology!

## Slide 18: Conclusions
LPWNA landscape is getting already crowded!
Debated aspects:
  Wideband or UNB?
  2.4 GHz or sub-GHz?
Not yet a definite answer to these questions and no objective comparisons (not biased by marketing) of the different solutions exist yet!

## Slide 19: Contacts
Andrea Zanella – zanella@dei.unipd.it

## Slide 20: Short range multihop
Pros
Very cheap
Low energy consumption
Cons
High complexity of large networks
Instability
Troublesome maintenance
See: https://www.youtube.com/watch?v=xUFUp-ylfC4

## Slide 21: Cellular-based solutions
Pros
Long range
Cons
Costs
Almost ubiquitous coverage
Well-established technology
Easy integration with rest of the world
Energy efficiency
Architectural limits
Notes: Pros
  Long range
  Almost ubiquitous coverage
  Well-established technology
  Easy integration with rest of the world
Cons
  Costs
    Terminal hardware costs are tens of dollars rather than the one or two dollar price point
    Subscription costs are high rather than a few dollars per year
  Energy efficiency
    Battery life cannot be extended much beyond a month
  Architectural limits
    GSM based networks are often ill-suited to the short message sizes typical in IoT use cases
    Significant overheads associated with signaling in order to move terminals from passive to active states

## Slide 22: LPWAN
Pros
Low cost
Very long range
Cons
Low bitrate
Long delays
Low power

## Slide 23: LoRa PHY
Proprietary modulation scheme derivative of Chirp Spread Spectrum (CSS)
  linear frequency modulated pulses whose frequency increases or decreases over a certain amount of time to encode information
Main advantages:
  processing gain due to spread spectrum technique
  high tolerance to frequency misalignment
  Support of variable Forward Error Correction codes and Spreading Factors
    possibility to trade throughput for coverage range/robustness/energy consumption while keeping constant bandwidth