## Slide 1: When bits get wet: introduction to microfluidic networking
Authors: Andrea Zanella, Andrea Biral
INW 2014 – Cortina d’Ampezzo, 14 Gennaio 2014
zanella@dei.unipd.it

## Slide 2: Purposes
Quick introduction to the microfluidics area
Overview of the research challenges we are working on…
Growing the interest on the subject… to increase my citation index! 

## Slide 3: Microfluidics… What is it all about?

## Slide 4: Microfluidics
Microfluidics is both a science and a technology that deals with the control of small amounts of fluids flowing through microchannels

## Slide 5: Features
MACROSCALE: inertial forces >> viscous forces
turbolent flow
microscale: inertial forces ≈ viscous forces
laminar flow
Notes: Specific characteristics:
  very low Reynolds number
    Re=inertial forces/viscous forces
    Re>4000  turbulent flow
    Re<1000  laminar flow
      viscous forces dominates inertial forces
      linear and predictable flow

## Slide 6: Advantages
Optimum flow control
  Accurate control of concentrations and molecular interactions
Very small quantities of reagents
  Reduced times for analysis and synthesis
  Reduced chemical waste
Portability

## Slide 7: Market
Inkjet printheads
Biological analysis
Chemical reactions
Pharmaceutical analysis
Medical treatments
…

## Slide 8: Popularity

## Slide 9: Recent papers (2014)

## Slide 10: Droplet-based microfluidics
Small drops (dispersed phase) are immersed in a carrier fluid (continuous phase)
very low Reynolds number (Re«1)
  Viscous dominates inertial forces
    linear and predictable flow
    generation of mono-dispersed droplets
low Capillary number (Ca«)
  surface tension prevail over viscosity
    cohesion of droplets

## Slide 11: Pure hydrodynamic switching principle
Two close droplets arrive at the junction
First drop “turns right”
Second drop “turns left”
Droplets flow along the path with minimum hydraulic resistance
Channel resistance is increased by droplets

## Slide 12: Microfluidic bubble logic
Droplet microfluidics systems can perform basic Boolean logic functions, such as AND, OR, NOT gates
A | B | A+B | AB
1 | 0 | 1 | 0
0 | 1 | 1 | 0
1 | 1 | 1 | 1

## Slide 13: Next frontier
Developing basic networking modules for the interconnection of different LoCs using purely passive hydrodynamic manipulation
  versatility: same device for different purposes
  control: droplets can undergo several successive transformations
  energy saving
  lower costs

## Slide 14: Challenges
Droplets behavior is affected by various intertwined factors
  flows in each channel depend on the properties of the entire system
    Topology & geometrical parameters
    Fluids characteristics (density, viscosity, …)
    Obstacles, imperfections, …
Time evolution of a droplet-based microfluidic network is also difficult to predict
    the speed of the droplets depends on the flow rates, which depend on the hydraulic resistance of the channels, which depend on the position of the droplets…

## Slide 15: Our contributions
Derive simple ``macroscopic models’’ for the behavior of microfluidic systems as a function of the system parameters
Define a simple Microfluidic Network Simulator framework
Apply the method to study the performance of a microfluidic network with bus topology

## Slide 16: “Macroscopic” models

## Slide 17: Basic building blocks
Droplet source
Droplet switch
Droplet use (microfluidic machines structure)

## Slide 18: Droplets generation (1)
Breakup in “cross-flowing streams” under squeezing regime

## Slide 19: Droplets generation (2)
By changing input parameters, you can control droplets length and spacing, but NOT independently!
(volumetric flow rate Qd)
(volumetric flow rate Qc)
Constant (~1)

## Slide 20: Experimental results

## Slide 21: Junction breakup
When crossing a junction a droplet can break up…
To avoid breakup, droplets shall not be too long… [1]
[1] A. M. Leshansky, L. M. Pismen, “Breakup of drops in a microfluidic T-junction”, Phys. Fluids, 21.

## Slide 22: Junction breakup
To increase droplet length you must reduce capillary number Ca  reduce flow rate  droplets move more slowly!
Non breakup

## Slide 23: Microfluidic Network Simulator

## Slide 24: Microfluidic/electrical analogy (I)
Syringe pump → current generator
Pneumatic source → voltage generator
Volumetric flow rate  Electrical current
Pressure difference  Voltage drop
Hydraulic resistance  Electrical resistance
Hagen-Poiseuille’s law  Ohm laws


## Slide 25: Microfluidic/electrical analogy (II)
Microfluidic channel filled only by continuous phase
↓
resistor with
Bypass channel (ducts that droplets cannot access)
↓
resistor with negligeable resistance
Microfluidic channel containing a droplet
↓
series resistor with

## Slide 26: Example
Droplet 1
Droplet 2
Droplet 1
Droplet 2
Droplet 1
Droplet 2
Droplet 1
Droplet 2
Droplet 1
Droplet 2
Droplet 1
Droplet 2
R1<R2  First droplet takes branch 1
R1+d>R2 
Second droplet takes branch 2

## Slide 27: Microfluidic Network Model
G(t)=(V,E)
  V={v1,…,vNnodes} E={e1,…,eNedges}

## Slide 28: Parallel with electrical network
Static MN graph is mapped into the dual electric circuit
  flow generator
  pressure generator
  microfluidic channel
  bypass channel

## Slide 29: Resistance evaluation
Each droplet is associated to its (additional) resistance which is added to that of the channel

## Slide 30: Simulation cycle
Compute the flow rates using Kirchhoff laws
Compute the motion of each droplet
Determine the outgoing branch when droplets enter junctions
Update the resistance of each channel depending on droplets position

## Slide 31: Simulative example

## Slide 32: Bus Network analysis

## Slide 33: Case study: microfluidic network with bus topology
Header
Payload

## Slide 34: Equivalent electrical circuit

## Slide 35: Topological constraints (I)
Header must always flow along the main path:
expansion factor
with a >1 
  Outlet branches closer to the source are longer

## Slide 36: Topological constraints (II)
Payload shall be deflected only into the correct target branch
Different targets require headers of different length
MM #N
MM #1
MM #2
Headers
HEADER RESISTANCE

## Slide 37: Microfluidic bus network with bypass channels

## Slide 38: Performance
Throughput
  volume of fluid conveyed to a generic MM per time unit (S [μm3/ms])
Access strategy
  “exclusive channel access”: one header-payload at a time!

## Slide 39
Bus network with simple T-junctions

## Slide 40
Bus network with bypass channels

## Slide 41: Conclusions and future developments
Addressed Issues:
  Definition of a totally passive droplet’s switching model
  Design of a macroscopic droplet-based Microfluidic Network Simulator
  Analysis of case-study: microfluidic bus network
A look into the future
  Joint design of network topology and MAC/scheduling protocols
  Design and analysis of data-buffer devices
  Proper modeling of microfluidics machines
  Characterization of microfluidics traffic sources
  Information-theory approach to microfluidics communications
  …

## Slide 42: When bits get wet: introduction to microfluidic networking
If we are short of time at this point… as it usually is,
just drop me an email… or take a look at my papers!
Any questions?

## Slide 43
Spare slides

## Slide 44: Microfluidic bubble logic
Recent discoveries prove that droplet microfluidic systems can perform basic Boolean logic functions, such as AND, OR, NOT gates.
A | B | A+B | AB
1 | 0 | 1 | 0
0 | 1 | 1 | 0
1 | 1 | 1 | 1

## Slide 45: Microelectronics vs. Microfluidics
 | Integrated circuit | Microfluidic chip
Transport quantity | Charge (no mass) | Mass (no charge)
Building material | Inorganic (semiconductors) | Organic (polymers)
Channel size | ~10-7 m | ~10-4 m
Transport regime | Similar to macroscopic electric circuits | Different from macroscopic fluidic circuits

## Slide 46: Key elements
Source of data
Switching elements
Network topology

## Slide 47: SOURCE: droplet generation

## Slide 48: Droplets generation (1)
Breakup in “cross-flowing streams” under squeezing regime

## Slide 49: Droplets generation (2)
By changing input parameters, you can control droplets length and spacing, but NOT independently!

## Slide 50: Junction breakup
When crossing a junction a droplet can break up…

## Slide 51: Junction breakup
To avoid breakup, droplets shall not be too long… [1]
[1]A. M. Leshansky, L. M. Pismen, “Breakup of drops in a microfluidic T-junction”, Phys. Fluids, 21.

## Slide 52: Junction breakup
Max length increases for lower values of capillary number Ca…
Non breakup

## Slide 53: Switching questions
What’s the resistance increase brought along by a droplet?
Is it enough to deviate the second droplet?
  Well… it depends on the original fluidic resistance of the branches…
  To help sorting this out… an analogy with electric circuit is at hand…
The longer the droplet, the larger the resistance
Dynamic viscosity

## Slide 54: Topological constraints (II)
Payload shall be deflected only into the target branch
Different targets require headers of different lengths
  rn : resistance increase due to header
  To deviate the payload on the nth outlet it must be
Main stream has lower resistance
nth secondary stream has lower resistance  payload switched
1st constraint on the value of the expansion factor a

## Slide 55: Topological constraints (III)
Header must fit into the distance L between outlets
Longest header for Nth outlet (closest to source)
Ln
Ln-1
Ln-2
2nd constraint on the value of the expansion factor a