## Slide 1: Signal processing: a networking perspective Part 2 – option B
Andrea Zanella
PhD Summer School of Information Engineering – 7-11 July, 2014 – Brixen (BZ)
zanella@dei.unipd.it
SIGnals processing & NETworking research group
SIGNET

## Slide 2: Outline
Part 3: QoE-oriented networking
  Mixing up PHY and application-layer signals
    smart environments
  Context awareness from signal processing
    SSIM characterization of video content
    Handover optimization
  Bye bye!
http://www.keepcalm-o-matic.co.uk/p/keep-calm-it-s-lunch-time/

## Slide 3: Exploiting complementarities
Pros
  Low cost
    Large networks with many devices
  Low energy consumption
    Possibility to power with small batteries or energy-scavenging
Cons
  Limited computing capabilities
  Limited memory
  Limited transmission range/speed
Cons
  High cost
    Single or few units
  High energy consumption
    Need for large batteries and/or recharging stations
Pros
  High computational capabilities
  Large memory
  Large energy capacity
  Large transmission range/speed
  Advanced mobility
Wireless Sensor Nodes (WSN)
Autonomous Mobile Robots (AMR)

## Slide 4: Application scenarios
Smart Environments
  AMRs may catalog, localize and retrieve objects upon request
  Libraries: AMRs may put back books on the shelves after closure
Assisted Living
  A portable device may drive a visual-impaired person through a partially unknown environment by vocally describing the smart objects that recognizes along the way
  A personal robot may display to a motion-impaired user the list of smart objects that it discovers
    remote controls, mobile phones, books, …
Dataset of object-models stored on the robot
  Low flexibility: new objects shall be included in the directory to be recognized
  Similar objects are indistinguishable
RFID-based communication
  Cheaper, but requires physical proximity and does not support sophisticated algorithms nor multi-hop communication
Application Scenarios
Limit of existing solutions

## Slide 5: Target application: autonomous exploration of unknown “smart” environments
AMR equipped with
  odometers for self-localization
  on-board camera
  RF transceiver
Smart Objects (SOs), i.e., common objects tagged with WSNs that provide
  Computational/communication capabilities
  data storage
  self-management features
Autonomous exploration of unknown environments and interaction with SOs
  No prior info about the number or kind of SOs
Vision
Goal

## Slide 6: Experimental Set up
250 kbps @ 2.4 GHz
Ultra low current consumption
Light, temperature, RSSI sensors
TinyOS
Home-made, based on Pioneer 2 ActivMedia platform
Linux OS with Miro middleware
ATX motherboard
  1,6 GHz Intel Pentium 4, 256 MB RAM, 160 GB HD
On-board camera
Odometers
TmoteSky sensor nodes
AMR Bender
TmoteSky connected to ATX via USB + MoteService class added to Miro

## Slide 7: System’s building blocks
Smart Object Identification
  The AMR gets a list of close by SOs, but does not know their location
Smart Object Mapping
  The AMR builds a map of the area estimating SOs’ location
Smart Object Recognition
  The AMR gets close to a selected object and, then, visually recognizes it in the image taken by the on-board camera

## Slide 8: Step 1. Smart Objects Identification

## Slide 9: Identification: centralized approach
ID=1, Laptop
ID=2, cellphone
ID=3, ashtray
ID=4, keys
ID=5, Tablet PC
Who’s out there?
ID | Object type
3 | ashtray
5 | Tablet PC
4 | Keys
1 | Laptop
2 | Cell phone
Smart Objects Lists

## Slide 10: Identification: distributed approach
Hello! I’m ID=1, Laptop
I know:
ID=3, ashtray
ID=5, Tablet PC
ID=4, Keys
Hello, I’m ID=2, cellphone
I know:
ID=3, ashtray
ID=5, Tablet PC
ID=4, Keys
ID=5, Laptop
Hello!
I am: ID=3, ashtray
I know: nobody
Hello! I’m ID=4, keys
I know:
ID=3, ashtray
ID=5, Tablet PC
Hello!
I’m: ID=5, Tablet PC
I know: ID=3, ashtray
Who’s out there?
ID | Object type
3 | ashtray
5 | Tablet PC
4 | Keys
1 | Laptop
2 | Cell phone
Smart Objects Lists
Hello, I’m ID=2, cellphone
I know:
ID=3, ashtray
ID=5, Tablet PC
ID=4, Keys
ID=5, Laptop

## Slide 11: Step 2. Smart Objects Mapping

## Slide 12: Mapping: still a challenge
GPS works pretty well… outdoor…
  Not that well indoor though!
  Hungry for energy (& money): not suitable for SOs
Cricket-like systems work fine, but require dedicated hw
  Impact on device size, cost, location, energy efficiency…
RF-based localization techniques are very attractive…
  if you’re not too picky about performance!
    Radio Signal Strength Indication (RSSI) is natively provided by all WSN platforms
    However, RSSI-based ranging is usually VERY noisy!

## Slide 13: Mapping: our solution
Improve RSSI-based ranging by using the communication capabilities of WSNs
  Multi-channel RSSI averaging
Use on-board odometers of the AMR and its computational capabilities to perform sophisticated localization algorithm
  SLAM: Simultaneous Localization (of the AMR) And Mapping (of the SOs)
WSN-wise
AMR-wise

## Slide 14: RSSI-based ranging: basics
Received power
Transmit power
Path loss coefficient
reference distance
environmental constant
transmitter-receiver distance
Deterministic component
Path loss channel model
  received power Pi @ distance di
Shadowing
Random term
Fast Fading
Ranging error
Propagation-based ranging

## Slide 15: RSSI-ranging: an example…
Random variations due to shadowing and fading obscure the log-decreasing law for the received power vs distance
Distance [mt]
Received power Pi [dBm]
Measured samples
Deterministic component

## Slide 16: Mitigating RSSI randomness
Shadowing term is actually due to strong and slowly time varying multipath interference
A shift in the carrier frequency will change the way reflected copies combine at the receiver

## Slide 17: Multi-channel RSSI: experimental results
Time Average
Frequency average

## Slide 18: RF-jumping protocol in a nutshell!
Anybody in CH1? (Next CH2)
I’m in CH1!
(Next CH2)
I’m in CH1!
(Next CH2)
Everybody’s switching on CH2. Let’s follow them!

## Slide 19: RF-jumping protocol
Set TX Channel to default RF Channel
FOR NextRFCh=1 TO 16 DO
  Send REQUEST(NextRFCh)
    Start REQ_TO
  WHILE NOT(REQ_TO expired) DO
    IF (REPLY pkt received)
      Store RSSI sample
      Restart REQ TimeOut
  ENDWHILE
  Set TX Channel to NextRFCh
ENDFOR
Set flag=false
IF (REQUEST pkt received)
  Get NextRFCh
  Set flag=true
  Set random REP_TO in [0,REQ_TO]
  WHILE NOT(REP_TO expired) DO
    IF (REPLY pkt received) & flag THEN Restart REP_TO
  ENDWHILE
  Send a REPLY pkt & switch to NextRFCh
IF (REPLY pkt received) & NOT flag THEN
  Get NextRFCh
  Switch to NextRFCh
AMR side
SO side

## Slide 20: Standard SLAM
Extended Kalman Filter
Odometry
RSSI Measures
Initialization
Motes pose and robot position estimation
Localization Algorithm:

## Slide 21: Standard SLAM result
Much better than standard WSN-only localization
Still large placement errors for WSNs

## Slide 22: SLAM with particle filter
Extended Kalman Filter
Odometry
RSSI Measures
Initialization
Particle Filter
Motes pose and robot position estimation
Localization Algorithm:

## Slide 23: Delayed Initialization based on Particle Filter
15

## Slide 24: Step 3. Smart Objects Recognition

## Slide 25: SO recognition by visual inspection
Feature matching under motion blur (Pretto et al. ICRA 2009)
The AMR should be able to recognize the objects from a description of the objects’ appearance
The object appearance is stored inside the object (in the motes)
The appearance is coded by scale invariant feature descriptors robust also to motion blur (MoBIF)

## Slide 26: Storing the appearance
5 meters
2 meters
1 meter
Enhancing robustness to scale:
  the object is imaged at different distances: near, medium, far
Enhancing robustness to rotation:
  the object is imaged every 20 deg.
Limiting descriptors size
  MoBIF descriptors extracted at different distances and angles are merged removing redundancy!

## Slide 27: MoBIF Matching
The AMR requires the selected SO to send its MoBIF descriptors
The AMR dynamically extracts MoBIF descriptor from the image taken by onboard camera
When MoBIF descriptors matching exceeds a threshold the SO is recognized
  matching is robust to scale, occlusion, illumination and rotation

## Slide 28: Conclusions
Synergetic combination of WSN and AMR:
  AMR helps WSN nodes localization
  WSN helps object recognition and handling by AMRs
  AMR & WSN together delivers new services
Future work:
  Improve localization by using also images taken by onboard camera into the SLAM algorithm
  Include smart navigation algorithms to the framework
  Adding object-handling algorithms to the system

## Slide 29: bibliography
E. Menegatti, M. Danieletto, M. Mina, A. Pretto, A. Bardella, S. Zanconato, P. Zanuttigh, and A. Zanella, "Autonomous discovery, localization and recognition of smart objects through WSN and image features" in the proceedings of the IEEE Globecom 2010 Workshop on Towards SmArt COmmunications and Network technologies applied on Autonomous Systems, 6 december 2010, Miami, Florida, USA.

## Slide 30: Context-awareness and reactiveness

## Slide 31: Cognition-based Network
Each node of the network:
  exploits local information to achieve its goal
  shares it with its neighbors
Self-adaptation to the environment to achieve network wide goals
Cognition applied to the entire network (not just at the PHY and MAC layers)

## Slide 32: Restricted Boltzmann Machines (RBM)
Stochastic neural network
  input layer symmetrically connected with a hidden layer of feature-detectors
Unsupervised learning of an internal model of the data
  features or latent causes

## Slide 33: Hierarchical processing
A key feature of cortical computation

## Slide 34: Example of learning/generation

## Slide 35: Example of applications
Content-based video management
Context-dependent handover in HetNets
Context-aware proactive content caching
…

## Slide 36: Multimedia growth
source:
Cisco report (2014)

## Slide 37: Challenges for video systems
Heavy data
Hierarchical system
Backhaul network capacity
Must handle different access
techniques
Needs to account for video popularity, heterogeneous user terminals
Quality-of-Experience of video is hard to capture
WiFi
3G
LTE

## Slide 38: Analysis
We consider a test set of 38 video clips, all encoded in an H.264-AVC format
All the videos are encoded with a 16-frame structure (1 I-frame, 15 P-frames) and compressed with 18 different rates
Depending on the content, the perceived quality of a compressed version changes
  We used the SSIM indicator to capture it

## Slide 39: Rate versus compression
Quantization point (compression level)
r=log(actual rate/original rate)

## Slide 40: SSIM versus rate
Self Similarity Index (SSIM)
r=log(actual rate/original rate)

## Slide 41: Remarks
All the video exhibit similar trends
  monotonic descent
  a steep “fall” after a threshold
However, quantitative differences mean
  different perceived end quality
  different resource requirements
These characteristics are more or less consistent within the same video

## Slide 42: Requirements for video delivery
QoE-based and content-aware resource allocation
  Rate-distortion curve depends on video content
  Video content affects size of the encoded video frames
  RBM can be used to infer rate-distortion curve of a video by observing the size (not the content) of video frames

## Slide 43: “Our” Video Classes

## Slide 44: RBM SSIM estimate

## Slide 45: Cognitive video admission control
Rate-based resource allocation
Cognitive QoE-based
resource allocation
Link rate over aggregate full-quality video rate

## Slide 46: Conclusions
need for consolidated understanding of the fundamental limits for
  massive access
  short packets
  extremely variable transmission patterns
Need for developing cognitive optimization modules that seamlessly interoperate at system level

## Slide 47: That’s all folks!