## Slide 1: Signal processing: a networking perspective Part 2 – option A
Andrea Zanella
PhD Summer School of Information Engineering – 7-11 July, 2014 – Brixen (BZ)
zanella@dei.unipd.it
SIGnals processing & NETworking research group
SIGNET

## Slide 2: Outline
Part 2: Signal processing at PHY/MAC layers
  The challenge of massive M2M access
    RFtag counting and identification
  Interference models & system capacity
    Multi-packet reception and Successive Interference Cancellation

## Slide 3: The challenge of massive M2M access
…
…
…
MTD
MTC link
Macro
Micro cell

## Slide 4: The shape of wireless to come
R1: today’s systems
R2: high-speed versions of today’s systems
R3: massive access for sensors and machines
R4: ultra-reliable connectivity at minimal rate
R5: physically impossible
5G=R1+R2+R3+R4
[Ref] F. Boccardi, R. W. Heath, A. Lozano, T. L. Marzetta, and P. Popovski, “Five Disruptive Technology Directions for 5G”,
IEEE Communications Magazine, February 2014.

## Slide 5: M2M reference architecture

## Slide 6: Machine Network Traffic
M2M devices generate traffics of the following types
  Periodic: smart metering application
  Event-driven: emergency event report
  Continuous: surveillance camera
Large volume of different types of traffic at core network
  Guarantee of diverse QoS traffic requirements
  Reliability of both human-to-human and M2M traffic

## Slide 7: high-speed wireless vs. M2M
high-speed systems built from information-theoretic principles with small control info and large data
M2M require short data packets from massive number of devices each transmitting sporadically

## Slide 8: enormous M2M growth expected
24-fold traffic growth from 2012 to 2017
4.6-fold growth of M2M #subscriptions
  from 369 million in 2012 to 1,7 billion in 2017
M2M traffic will account for approximately 5 % of overall mobile traffic in 2017
© CISCO Visual Networking Index
Chart: 
| 2012.0 | 2013.0 | 2014.0 | 2015.0 | 2016.0 | 2017.0
PB/month | 23.5 | 44.3563 | 83.7224 | 158.0261 | 298.2742 | 562.9926
global M2M traffic

## Slide 9: The batch resolution problem
SIGnals processing & NETworking research group
SIGNET

## Slide 10: Problem statement
What’s a “batch”?
  Set of mutually interfering nodes simultaneously solicited to send a packet
    RF tags illuminated by a reader
    Wireless nodes that reply to neighbour-discovery request
    Mobile terminals that compete to reserve a channel slot
What’s the “Batch resolution problem”?
  Simultaneous transmissions by multiple nodes result into collision  all packets are lost!
  Nodes need to arbitrate the channel access in order to transmit their packet avoiding collisions
    A node that successfully transmits is said to be resolved
What’s a “Batch Resolution Algorithm” (BRA)?
  The BRA arbitrates the channel access in order to minimizing the batch resolution interval, ie, the mean time required to resolve all the nodes in the batch
Broadcast inquiry message
Solicited nodes form the “batch”
Inquirer
Unicast reply messages

## Slide 11: Batch resolution problem vs MAC
The batch resolution problem resembles the MAC problem but…
  MAC protocols generally look at the channel contention as a steady-state phenomenon
  BRAs address scenarios where contention has a bursty nature

## Slide 12: Performance measures
Batch resolution interval (BRI)
  T(n) = E[time required to resolve a batch of size n]
Batch Throughput
Asymptotic throughput
  Maximal sustainable arrival rate when BRA is used as obvious MAC:
    solve a batch and queue packets arriving in the meanwhile, the form the next batch (gate policy)

## Slide 13: Splitting-tree BRAs
Time is slotted
  Slots may have unequal duration in CSMA networks
In each slot, some nodes are activated, i.e., transmit
Immediate feedback: returned after each slot
  Idle slot: no nodes transmit
  Successful slot: a single node transmit
  Collided slot: two or more nodes transmit
BRA works recursively, driven by feedback

## Slide 14: Divided batch in “m” subgroups
Initial batch
(expected size mn)
Subgroup 1
Subgroup 2
Subgroup m
(expected size g=mn/m optimal)

## Slide 15: Slot1: collided
Initial batch: {1,2,3,4,5}
L= {1,2}
R= {3,4,5}

## Slide 16: Slot2: collided
Initial batch: {1,2,3,4,5}
L= {1,2}
LL= {1,2}
LR= { }
R= {3,4,5}

## Slide 17: Slot3: collided
Initial batch: {1,2,3,4,5}
L= {1,2}
LL= {1,2}
LR= { }
R= {3,4,5}
LLL= {1}
LLR= {2}

## Slide 18: Slot4: successful
Initial batch: {1,2,3,4,5}
L= {1,2}
LL= {1,2}
LR= { }
R= {3,4,5}
LLL= {1}
LLR= {2}
1 is resolved

## Slide 19: Slot5: successful
Initial batch: {1,2,3,4,5}
L= {1,2}
LL= {1,2}
LR= { }
R= {3,4,5}
LLL= {1}
LLR= {2}
1 is resolved
2 is resolved

## Slide 20: Slot6: idle
Initial batch: {1,2,3,4,5}
L= {1,2}
LL= {1,2}
LR= { }
R= {3,4,5}
LLL= {1}
LLR= {2}
1 is resolved
2 is resolved

## Slide 21: Slot7: collided
Initial batch: {1,2,3,4,5}
L= {1,2}
LL= {1,2}
LR= { }
R= {3,4,5}
LLL= {1}
LLR= {2}
1 is resolved
2 is resolved
RL= {}
RR= {3,4,5}

## Slide 22: Slot8: idle
Initial batch: {1,2,3,4,5}
L= {1,2}
LL= {1,2}
LR= { }
R= {3,4,5}
LLL= {1}
LLR= {2}
1 is resolved
2 is resolved
RL= {}
RR= {3,4,5}

## Slide 23: Slot9: collided
Initial batch: {1,2,3,4,5}
L= {1,2}
LL= {1,2}
LR= { }
R= {3,4,5}
LLL= {1}
LLR= {2}
1 is resolved
2 is resolved
RL= {}
RR= {3,4,5}
RRL= {3}
RRR= {4,5}

## Slide 24: Slot10: successful
Initial batch: {1,2,3,4,5}
L= {1,2}
LL= {1,2}
LR= { }
R= {3,4,5}
LLL= {1}
LLR= {2}
1 is resolved
2 is resolved
RL= {}
RR= {3,4,5}
RRL= {3}
RRR= {4,5}
3 is resolved

## Slide 25: Slot11: collided
Initial batch: {1,2,3,4,5}
L= {1,2}
LL= {1,2}
LR= { }
R= {3,4,5}
LLL= {1}
LLR= {2}
1 is resolved
2 is resolved
RL= {}
RR= {3,4,5}
RRL= {3}
RRR= {4,5}
RRRL= {4}
RRRR= {5}
3 is resolved

## Slide 26: Slot12: successful
Initial batch: {1,2,3,4,5}
L= {1,2}
LL= {1,2}
LR= { }
R= {3,4,5}
LLL= {1}
LLR= {2}
1 is resolved
2 is resolved
RL= {}
RR= {3,4,5}
RRL= {3}
RRR= {4,5}
RRRL= {4}
RRRR= {5}
3 is resolved
4 is resolved

## Slide 27: Slot13: successful
Initial batch: {1,2,3,4,5}
L= {1,2}
LL= {1,2}
LR= { }
R= {3,4,5}
LLL= {1}
LLR= {2}
1 is resolved
2 is resolved
RL= {}
RR= {3,4,5}
RRL= {3}
RRR= {4,5}
RRRL= {4}
RRRR= {5}
3 is resolved
4 is resolved
5 is resolved

## Slide 28: Modified Binary Tree
Avoid predictable collision
  A “collidedidle” sequence is always followed by a collided slot!
collided
idle
collided

## Slide 29: Modified Binary Tree
Solution: virtualize predictable collisions
Any time a collided slot is followed by an idle slot, do not activate the right subset, but rather, split it in two subsets as if a collision had occurred (but without wasting a slot)

## Slide 30: Slot7: collided
Initial batch: {1,2,3,4,5}
L= {1,2}
LL= {1,2}
LR= { }
R= {3,4,5}
LLL= {1}
LLR= {2}
1 is resolved
2 is resolved
RL= {}
RR= {3,4,5}

## Slide 31: Slot8: idle  split immediately!!!
Initial batch: {1,2,3,4,5}
L= {1,2}
LL= {1,2}
LR= { }
R= {3,4,5}
LLL= {1}
LLR= {2}
1 is resolved
2 is resolved
RL= {}
RR= {3,4,5}
RRL= {3}
RRR= {4,5}

## Slide 32: Slot9: successful
Initial batch: {1,2,3,4,5}
L= {1,2}
LL= {1,2}
LR= { }
R= {3,4,5}
LLL= {1}
LLR= {2}
1 is resolved
2 is resolved
RL= {}
RR= {3,4,5}
RRL= {3}
RRR= {4,5}
3 is resolved

## Slide 33: Clipping mechanism
Valid for batches with Poisson distributed size
When a collided slot is followed by another collided slot, the right branches of the tree can be clipped
  The second collision “erase” the prior information on the cardinality of the nodes in the right subsets
  It is more convenient to return these nodes to the original set and divide again in optimal subsets

## Slide 34: Rationale
Let X be the size of the activated interval
  X is a Poisson rv with parameter m
Imagine to split BEFORE observing the outcome
  L and R are independent Poisson rvs with parameters mp and m(1-p)
Now, you observe a collision X>1  R is not Poisson!
  Pr[R=k | L+R >1]
If another collision  L>1  R is again Poisson!
  Pr[R=k | L+R >1, L>1] = Pr[R=k | L>1] = Pr[R=k]

## Slide 35: Slot1: collided
subgroup: {1,2,3,4,5}
L= {1,2}
R= {3,4,5}
Residual batch

## Slide 36: Slot2: collided
L= {1,2}
LL= {1,2}
LR= { }
R= {3,4,5}
Residual batch

## Slide 37: Slot3: collided
L= {1,2}
LL= {1,2}
LR= { }
LLL= {1}
LLR= {2}
Residual batch

## Slide 38: Slot4: successful
L= {1,2}
LL= {1,2}
R= {3,4,5}
LLL= {1}
LLR= {2}
1 is resolved
Residual batch

## Slide 39: Slot5: successful
L= {1,2}
LL= {1,2}
R= {3,4,5}
LLL= {1}
LLR= {2}
1 is resolved
2 is resolved
Residual batch

## Slide 40: Interval Estimate Collision Resolution algorithm (IECR)
CMBT is optimal if mean batch size mn is known
If the batch size is unknown, it must be estimated before applying CMBT
IECR couple CMBT with a batch size estimate phase
  Apply CMBT to whole batch until the first successful transmission
  Estimate the residual batch size n on the basis of the number of consecutive collisions undergone so far
  Repeat by assuming n as estimated above

## Slide 41: Timing
activated
backlogged
resolved
I/S/C
Idle slot
Feedback packet
Collided slot
Successful slot
C
I
C
S
S
S
tc
bp
ti
ts
Event | Slot duration | Feedback duration |  | 
 |  |  | Classical | Practical (CSMA)
Successful | Tdata=1 | fs | negligible | significant
Idle | bi<<1 | fi | negligible | negligible
Collision | bc~1 | fc | negligible | small

## Slide 42: The cost of neglecting feedback cost…
The larger the ACK tx time (fs)
the lower the asymptotic throughput
of immediate-feedback BRAs

## Slide 43: A different approach: deferred feedback strategies

## Slide 44: Classical Dynamic Framed Slotted Aloha
Framed Slotted ALOHA (FSA)
  Slots are organized in frames of W slots
  In each frame, nodes transmit in random slots
  Feedback is returned only at the end of the frame by using a probe packet
Dynamic FSA
  Frame size is adjusted dynamically to maximize the expected per-frame throughput
Drawback: probing cost is neglected!
  Maximizing per-frame throughput does not necessarily minimize the overall batch resolution interval

## Slide 45: Our proposal
ABRADE: Adaptive Batch Resolution Algorithm with Deferred Feedback
  Basically a dynamic framed slotted ALOHA with a novel frame-adaptation strategy that keeps into account all costs!
  Batch size n is assumed to be known beforehand!
ABRADE+: couple ABRADE with a batch size estimate algorithm
  No prior knowledge about the batch size

## Slide 46: ABRADE in a nutshell
Assumption: the (residual) batch size “n” is known
The frame size wn of the next round is selected in order to minimize the overall Batch Resolution Interval (BRI) for that batch
Frame duration
Residual batch resolution interval
  w*n: optimal frame length for a batch of size n
  pw,n(s) = Pr[s|w,n]
Dynamic programming optimization
  BRI for batch
  of size n
number of successful collided idle slots in the frame
Frame Size
Batch
Size

## Slide 47: Optimal frame length
--- bp=2
___ bp=1

## Slide 48: ABRADE’s throughput
l(n)
Optimal number of transmissions per slot

## Slide 49: ABRADE+: batch size estimate
ABRADE needs prior knowledge of the batch size n
In most cases, n is unknown and needs to be estimated
Estimate can be refined as the batch resolution proceeds
ABRADE+ is as ABRADE with two add-ons
    Batch Size Estimate Function (BSEF)
    Start up phase

## Slide 50: Quick survey of most-known BSEFs
V=<s,c,i>  estimate of n
  [Schoute83]:
  [Cha&Kim05]:
  [Vogt02]:
  [Khandelwat06]:
  [Kodialam06]:
  [Zanella12]:

## Slide 51: A glance at BSEFs performance
Mean Square Estimate Error (MSE)

## Slide 52: Start up phase
What frame size w0 shall be used at the very fist cycle?
  w0 shall be small, to have a first estimate of n as soon as possible
  w0 shall be large to avoid many collisions
Solution: Probabilistic Framed Slotted Aloha
  Nodes transmit with probability p
Issue: p, w0 shall be set to strike a balance between estimate accuracy & performance loss

## Slide 53: Setting p and w0
Let mn be the mean batch size n
  if unknown, arbitrarily assumed equal to Nmax/2
Set p such that w0 is optimal for a batch size equal to pmn:
Set w0 such that the mean square estimate error, MSE(p) is lower than Dmn, where D is a design parameter

## Slide 54: Initial frame size vs D
White marker: b=0.0654
Black marker: b=0.0225
shorter frame sizes
yield much worse MSE
lower MSE requires
much larger frame sizes

## Slide 55: Case study
Parameters set according to WiFi (WF) & ZigBee (ZB) specifications
Batch size n with Poisson distribution of known mean N
Batch size totally unknown to the algorithm
  mn arbitrarily set to 100
  D=0.6
 | Tdata [ms] | b | bs | bc | bp=w/Lmax
 | 0.399 | 0.0225 | 0.1319 | 0.1319 | w/18496
 | 4.896 | 0.0654 | 0.1111 | 0.0458 | w/944

## Slide 56: 1. Poisson: Throughput
Asymptotic throughput gain of ~9% for WF and ~6% for ZB
Performance crossing for batches of small size
Slightly worse for extremly small batches
  Pay the cost of long probe message
ABRADE+
ABRADE+
FCFS
FCFS

## Slide 57: 2. Unknown: Throughput
Throughput gain is maintained also in the case of unknown batch size, as long as the batch is larger than few units
Gain is more evident for WF than ZB
ABRADE
ABRADE
Perfomance contraction due to initial parameter setting (mn=50)

## Slide 58: Summarizing
The batch resolution problem is still challenging
  Count and identify RFtags
  Bunch of sensors replying to probes
Analysis shall carefully consider all protocol layer aspects
  Initialization & feedback may have dramatic impact
Large literature, but still much to be done!

## Slide 59: Main bibliography
J. Capetanakis, “Tree algorithms for packet broadcast channels,” IEEE Trans. on Information Theory, vol. 25, no. 5, pp. 505–515, Sep. 1979.
R. Gallager, “Conflict resolution in random access broadcast networks,” in AFOSR Workshop Commun. Theory Appl., Sep. 1978, pp. 74–76.
Zanella, A., "Adaptive Batch Resolution Algorithm with Deferred Feedback for Wireless Systems," Wireless Communications, IEEE Transactions on , vol.11, no.10, pp.3528,3539, October 2012
A. Zanella "Estimating Collision Set Size in Framed Slotted Aloha Wireless Networks and RFID Systems". IEEE Communications Letters, Volume 16, Issue 3, pp: 300-303, March 2012

## Slide 60: Improving M2M cell capacity
Exploiting multipacket reception capabilities and SIC

## Slide 61: The problem
Reference scenario:
  one base station, multiple transmitters, uplink channel
The problem:
  How many transmitters can be served?
  What’s the maximum cell capacity?
  How can we get it?
TX1
TX2
TX3
TXj
TXn
Pj
Pn
P1
P2
P3
RX

## Slide 62: The literature
Classic Aloha model [Kleinrock75]:
  Destructive interference: one single transmission at a time
  Max throughput: S = 1/(2e)
  Slotted version: S = 1/e
Smax = 1/(2e)
Smax = 1/e

## Slide 63: Capture
Capture phenomenon [LauLeung, TCOM92]
  When the various signals are received with significantly different powers  capture effect may take place
  the strongest signals may survive the collision and be correctly decoded
Generalization: “Capture” occurs when one or more of the overlapping signals are successfully decoded by the receiver despite the interference

## Slide 64: Capture models
Statistical geometry model [Roberts, ComRev75]
  Intended signal is captured when the strongest interferer is sufficiently far apart from the receiver
  Doesn’t account for actual signal propagation phenomena nor does it consider cumulative effect of multiple “weak” interferers
Arrival Time model [Davis&Gronemeyer, TCOM80]
  Intended signal is captured when arrival instants of the first and second signals are sufficiently apart
  Doesn’t account for signal strengths, nor for simultaneous transmissions

## Slide 65: Other capture models
Counting model [Wieselthier et al, TCOM89]
  Capture occurs with probability that depends on the number of overlapping signals
  Doesn’t account for actual signal powers
  At most one capture per transmission attempt
Power model [Ephremides&Luo, TIT02]
  Capture if no other signal with higher power overlaps in time
  Doesn’t account for cumulative effect of multiple “weak” interferers

## Slide 66: MPR and Stability
MPR & Stability [Ghez, Verdu, Schwartz, ITAC88]
  They assume a given pmd for the number r of captured signals out of a collision of n overlapping signals
  Show that MPR can stabilize ALOHA and that max throughput is Smax = E[r]
  Don’t give an expression for the pmd of r given n

## Slide 67: Physical capture model
Decoding model: SINR threshold
Use of strong coding to achieve Shannon capacity
N0: noise power (neglected)
gj : SINR of the j-th signal
b : capture threshold
Pj : power of the j-th signal at the receiver
TX1
TX2
TX3
TXj
TXn
Pj
Pn
P1
P2
P3
RX
  gj > b j-th signal is correctly decoded (capture)
  gj < b  j-th signal is collided (missed)
  Aggregate
  interference

## Slide 68: Multi Packet Reception
MPR can be enabled by means of
  Signal spreading (DSSS)
    b<1 multiple signals (up to 1/b) can be captured at a time
  Successive interference cancellation (SIC)
    Capture signal j with SINR gj>b
    Reconstruct and cancel signal j from the overall received signal
      Cancellation leaves a fraction z of residual interference power
    Repeat iteratively

## Slide 69: Open questions
Number of simultaneous transmissions (n)
Statistical distribution of the receiver signal powers (Pi)
Capture threshold (b)
Max number of SIC iterations (K)
Interference cancellation ratio (z)
System parameters
Capture probability?
System throughput?

## Slide 70: The answer
Capture probability
  Cn(r;K)=Pr[r signals out of n are captured within at most K SIC cycles]
  Computing Cn(r;K) is difficult because the SINRs are all coupled!!!
  E.g.
  Computation of Cn(r;k) becomes more and more complex as the number n of signals increases
SIC makes things even worse

## Slide 71: State of the art
Narrowband (b>1), No SIC (K=0)
  [Zorzi&Rao,JSAC1994,TVT1997] derive the probability Cn(1;0) that one signal is captured
    MPR and SIC are not considered
Wideband (b<1), No SIC (K=0)
  Can capture multiple signals in one reception cycle
  [Nguyen&Ephremides&Wieselthier,ISIT06, ISIT07] derive the probability 1-Cn(0;0) that at least one signal is captured
    Expression involves n folded integrals, does not scale with n
Wideband (b<1)+SIC (K>0)
  [ViterbiJSAC90] shows that SIC can achieve Shannon capacity in AWGN channels
    Requires suitable received signals power allocation
  [Narasimhan, ISIT07] studies outage rate regions in presence of Rayleigh fading
    Eqs can be computed only for few users
  [Weber et al, TIT07] study SIC in ad hoc wireless networks
    Derive bounds on the transmission capacity based on stochastic geometry arguments

## Slide 72: State of the art
Wideband (b<1) + SIC (K>0) (cont)
  [ZanellaZorzi, TCOM2012] provide a scalable method for the numerical evaluation of the capture probability distribution Cn(r;K)
    Investigate capture distribution & system throughput when varying system parameters {n,b,K,z}
  Provide approximate expressions for the capture probability and the MPR throughput

## Slide 73: Capture probability for pure MPR case
No SIC (K=0)

## Slide 74: Problem statement
The capture condition can be expressed as
  b’ is termed modified capture threshold
  b’L is named absolute capture threshold
We aim at determining the expression of
  Cn(r)=Pr[r signals out of n are captured]

## Slide 75: Capture distribution
Because of the problem symmetry we have
r captured signals
n-r missed signals
and applying Bayes’ rule: P[A|B]P[B] = P[B|A]P[A]
Conditioning on L=x we get…
iid

## Slide 76: Conditioned aggregate received power Lr
The issue is now to compute the PDF
We introduce the auxiliary r.v.
gives the aggregate power given that r signals are above u, and n−r are below u setting u=xb’ we get
iid rvs with PDF
fa(u)(x)=fP(x|P>u)
iid rvs with PDF
fb(u)(x)=fP(x|P≤u)
Notes: f_{\Lambda_r} is the PDF of the conditioned aggregate received power r, defined as the aggregate power given that r signals have power above the threshold rb′, and n − r have power below such a threshold.

## Slide 77: Auxiliary random variable
Since ah(u) and bh(u) are independent, we get
Putting all the pieces together we get the final expression
Inverse Fourier Transform
Fourier Transform
Notes: \alpha(u) and \beta(u) are independent r.v.s which are the conditioned versions of the r.v.s that describe the received power. More specifically, the PDF of alpha(U) and \beta(u) is equal to the PDF of the r.v. Pj, conditioned to Pj>u and Pj<=u, respectively. Therefore, we an intuitive *though formally worng) notation, we can write f_{alpha(u)}(a)~Pr[P=a | P>u]; and f_{beta(u)}(a)~Pr[P=a | P<u];
The rvs are now independent and the PDF of their sum is just the multifold convolutions of f_{alpha(u)}(a) and f_{beta(u)}(a). In the frequency domain, this convolution becomes the product of the FTs of the PDFs. Taking the IFT, we then get the PDF of the auxiliary r.v. \tilde \Lambda_r(u).

## Slide 78: Capture distribution: approximate expression
If n›› & r=0 or r=n or r≈n/2 the central limit theorem applies
from which we get the following approximate expression of Cn(r):

## Slide 79: Throughput
k: reception capability
  max number of signals that can be simultaneously decoded
Sn(k): average number of signals captured by a system with reception capacity k and a collision size n
Note: previous literature focused on Sn(1)=1-Cn(0) only!

## Slide 80: Analysis of the SIC case

## Slide 81: Notation: reception set and vector
n : number of overlapping signals
r : overall number of decoded signals
h ={0,1,…,K}: SIC iteration
Uh: set of signals decoded at the h-th SIC iteration
  Uk+1: set of missed signals at the end of the reception process
r=[r0,r1,…,rk,rk+1]: reception vector
  rh=|Uh|, rk+1=|Uk+1|= n-r
r ={ r0, …, rh , …. rk, rk+1 }
TX1
TX2
TXj
TXr
TXr+1
TXn
U={ U0, …, Uh, …. Uk, Uk+1 }
decoded
missed

## Slide 82: Notation: aggregate power
Set of signal powers for users in Uh
Aggregate power of users in Uh
Overall sign. power at the h-th decoding cycle

## Slide 83: Visually
TX1
TX2
TXj
TXr
TXr+1
TXn
P={ P0, …, Ph , …. Pk, Pk+1 }
G={ G0, …, , …. Gk, Gk+1 }
L={ L0, …, , …. Lk, Lk+1 }
z
z
z

## Slide 84: Step 1: a bit of combinatorial analysis
Ordered
probability distribution
Combinatorial coefficient

## Slide 85: Step 2: express decoding probability in terms of Pj
Signals in Uh are decoded at the h-th SIC iteration if
  were not decoded at previous iterations
  verify capture condition after h SIC iterations
Mathematically
Considering all k SIC iterations…
where

## Slide 86: Step 3: let’s start conditioning
The capture threshold at each SIC iteration are
Conditioning on {Gh=gh} the capture thresholds becomes deterministic
Then, we can write (we omit g in the argument of lh)
Aggregate power of signals in Ui
PDF of the random vector G
evaluated in g=[g0,...,gk+1]
k+2 nested integrals

## Slide 87: Step 4: swap terms
Applying Bayes rule we get
The issue now is to compute this conditional probability
iid
l-1=-∞
iid

## Slide 88: Step 5: aux variables help decoupling terms
Each Gh is the aggregate power of the signals in Uh given that they are in the interval (lh-1,lh]
We then define
where ah,i(u,v) are iid with PDF
Hence, for any given g, we have
Fourier Transform

## Slide 89: Step 6: put all pieces together
Number of nested integrals grows linearly with number K of SIC iterations, not with n
  Equation can be computed for large values of n, provided that the number of SIC iterations remains reasonable (5÷6)
Central limit theorem can be invoked for sufficiently large rh

## Slide 90: Throughput
Sn(k): average number of signals captured by a system wit collision size n and at most K SIC iterations
Exact expression:
Approximate (iterative) expression
Where is the approximate mean number of signals decoded at the h-th SIC iteration

## Slide 91: Approximate mean number of captures: first reception
Iteration h=0: number of undecoded signals n0=n
  Compute capture threshold
  Approximate capture condition
  Mean number of decoded signals
  Residual interference power

## Slide 92: Approximate mean number of captures: first reception
Iteration h>0: number of undecoded signals:
  Compute capture threshold
  Approximate capture condition
  Mean number of decoded signals
  Residual interference power
Residual interf.
Interf. from undecoded signals

## Slide 93: Case study

## Slide 94: Case study
Pure Path Loss (PL)
TXs uniformly distributed within a circle of radius R centered at RX
Rayleigh Fading (RF)
TXs at equal distance from RX (or long-term power control) but signals affected by multi-path fading
LogNormal (LN)
TXs at equal distance from RX (or short-term power control) but nominal signals power affected by small Gaussian noise [dBm]
PathLoss & Rayleigh fading (PLRF)
TXs uniformly scattered around RX, within a disk of radius R with signals affected by independent Rayleigh fading

## Slide 95: Cn(r) in PL scenario
When n << 1/b’, all signals are captured with high probability
When n > 1/b’, the distribution of the number of signals captured is bell-shaped
When n >> 1/b’, fewer and fewer signals are captured
r ≤ 1/b’=51
Notes: When n is well below 1/b′ =51, which gives an upper bound on the number of signals that can be potentially captured, then the curves present a spike in r = n because the most likely event is that all the n signals
are captured (full capture).
When n increases, the full capture probability decreases and the distribution roughly assumes a bell-shaped form, with mean and variance that progressively decrease. Finally, for very large values of n, Cn(0) tends to increase, and the system can capture fewer and fewer signals.

## Slide 96: Throughput in PL & PLRF
r ≤ 1/b’=11
S(6)≅S(11)

Max performance are closely approached even with partial reception capability.
Rayleigh fading augments diversity of received signal strength & increases capture probabilities for large values of n
Notes: It is interesting to note that increasing the reception capability k beyond a certain point yields diminishing returns. For example, in the case shown k = 6 already provides a throughput very close to the maximum
possible. This result suggests that it is possible to design radio systems with partial reception capability that attain the same performance as systems with full reception capability.
The presence of Rayleigh fading augments the diversity of the received signal strength, thus increasing the capture probabilities for large values of n.

## Slide 97: Approximate vs exact expressions
 | RF | PLRF
Exact |  | 
Approximate |  | 
Sn(1)=1-Cn(0)=Pr[capturing at least one signal]
  metric considered in most of the previous literature
The accuracy of the approx. of Cn(0) is very good in all the considered cases
The approximation of Cn(r) is not very good when either r or n-r are positive but small (not shown here)
Notes: Compares the throughput S_n(1) of systems with single reception capability k=1 (the metric considered in most of the previous literature). Solid curves refer to the RF case, whereas dashed curves are used for the PLRF scenario. The exact results (marks) are compared with the approximate values (lines) obtained using $\tilde C_n(0)$ in place of $C_n(0)$ in \eq{Snk}. As can be noted, the accuracy of the approximation is very good in all the considered cases.

## Slide 98: Performance with SIC
Rayleigh channel only

## Slide 99: Capture probability distribution
Multiple SIC (K>1): capture probability keeps improving, but gain reduces
One SIC (K=1): likely to decode 4÷10 signals, double capture capabilities!!!
No SIC (K=0): likely to decode 2÷5 signals
n=20, b=0.1, z=0.1
K increases

## Slide 100: Throughput vs n
b=0.1, z=0.1
exact
approximate
K increases
High congestion
Low congestion
Max SIC gain ~500%
Approximation is quite good!
optimal # of concurrent transmissions

## Slide 101: Max SIC gain analysis
SIC is more effective with small b
The less residual interference, the larger the SIC gain
For K>1/z, SIC gain is negligible
  Empirical conjecture

## Slide 102: An example of application to network planning
Goal: dimensioning an MPR access point
Given parameters:
  Users’ spatial distribution: Poisson process with density d
Performance metric: average throughput SD(K)=E[Sn(K)]
Knobs
  Cell radius: D
  Capture threshold: b
  MPR capability: R
  SIC capability: K
  Power control capabilities
    NoPC: No power control  Path Loss propagation model (PL)
    SPC: Slow power control  Rayleigh Fading (RF)
    FPC: Fast power control  LogNormal (shadowing) fading (LN)

## Slide 103: 1st step: determine throughput when varying cell radius with infinite MPR and no SIC
Optimal cell radius depends on
the power control capabilities
No Power Ctrl
Slow Power Ctrl
Fast Power Ctrl
The better the Power Ctrl
the higher the peak rate but
the less robust to variations in population size
No power control yields
lower but more stable throughput

## Slide 104: 2nd step: determine the number of MPR cycles
Focusing on the No Power Control case we set the cell radius to D=50m
Using our equations we find the minimum MPR capability Rm of the receiver beyond which the performance gain becomes negligible
  we can set Rm = arg minR{Sn(R)/Sn(∞) ≥ 1 − ρ} where ρ is the maximum acceptable performance loss
  In our example, Rm=15 yields less than 10% of throughput loss

## Slide 105: 3rd step: introduce SIC
No Power Ctrl
Slow Power Ctrl
Fast Power Ctrl
With just 1 SIC cycle
No SIC

## Slide 106: Asymptotic performance
Zanella et al. “M2M massive wireless access: challenges, research issues, and ways forward” – Globecom 2013
Notes: A BS capable of performing perfect SIC and MPR can theoretically decode an arbitrary large number of simultaneous transmissions by proportionally reducing the per-user data rate, in such a way that the aggregate system capacity remains almost constant. Furthermore, the capacity of the cell depends on the statistical distribution of the signal powers: generally, the higher the variance, the more effective the SIC and, then, the larger the asymptotic aggregate capacity.

## Slide 107: Bibliography
C. Lau and C. Leung, “Capture models for mobile packet radio net- works,” IEEE Transactions on Communications, vol. 40, pp. 917–925, May 1992.
L. G. Roberts, “ALOHA packet system with and without slots and capture,” Communications Reviews, pp. 28–42, April 1975.
D. H. Davis and S. A. Gronemeyer, “Performance of slotted ALOHA random access with delay capture and randomized time of arrival,” IEEE TCOM80
J. E. Wieselthier, A. Ephremides, and L. A. Michaels, “An exact analysis and performance evaluation of framed ALOHA with capture,” IEEE TCOM89
A. Ephremides and W. Luo, “Power levels and packet lengths in random multiple access,” IEEE TIT, vol. 48, pp. 46–58, Jan. 2002.
S. Ghez, S. Verdu, and S. Schwartz, “Stability properties of slotted Aloha with multipacket reception capability,” IEEE Transactions on Automatic Control, vol. 33, no. 7, pp. 640 –649, jul 1988.
C. Namislo, “Analysis of mobile radio slotted ALOHA networks,” IEEE JSAC, vol. 2, pp. 583–588, July 1984.
M. Zorzi and R. Rao, “Capture and retransmission control in mobile radio,” IEEE JSAC, pp. 1289–1298, Oct. 1994.
X. Wang and J. J. Garcia-Luna-Aceves, “Embracing interference in ad hoc networks using joint routing and scheduling with multiple packet reception,” in IEEE INFOCOM 2008, 13-18 April 2008, pp. 843–851
J. J. Garcia-Luna-Aceves, R. Sadjadpour, Hamid, and Z. Wang, “Chal- lenges: towards truly scalable ad hoc networks,” MobiCom’07
A. Zanella, and M. Zorzi "Theoretical Analysis of the Capture Probability in Wireless Systems with Multiple Packet Reception Capabilities" IEEE Transactions on Communications, vol.60, no.4, pp.1058-1071, April 2012
Zanella et al. “M2M massive wireless access: challenges, research issues, and ways forward” – Globecom 2013

## Slide 108: Spare slides

## Slide 109: Break!!!! We all need it!

## Slide 110: Bluestein FFT algorithm
FFT samples are equally spaced over the entire signal bandwidth
When raising the FTs to a power >1 most of such samples reduce to zero!
Bluestein's FFT algorithm (BFFT) ``squeezes’’ the samples into a fraction of the original bandwidth, so that samples are still significant after power raising

## Slide 111: Rayleigh fading
Exponential distribution of the received power Pj
Fourier Transform of the auxiliary rv a(u,v)
Mean value of a(u,v)

## Slide 112: Appendix: asymptotic throughput

## Slide 113: Appendix: asymptotic throughput
Taking the derivative wrt mu_infty

## Slide 114: 1. Poisson: Energy efficiency
Mean number of tx per slot (proportional to energy consumption) comparable to the best performing algorithms
ABRADE
ABRADE

## Slide 115: massive asynchronous access
approach
  move complexity to BS
  use advanced MAC/PHY
    MPR: multi packet reception
    SIC: successive interference cancellation
TX1
TX2
TX3
TXj
TXn
Pj
Pn
P1
P2
P3
RX

## Slide 116: SIC+MPR throughput
b=0.1, z=0.1
# of SIC iterations
High congestion
Low congestion
Max SIC gain ~500%
optimal # of concurrent transmissions
A. Zanella, and M. Zorzi, "Theoretical Analysis of the Capture Probability in Wireless Systems with Multiple Packet Reception Capabilities" IEEE Transactions on Communications, 2012
Notes: SIC gain increases with # of cancellation cycles, up to an asymptotic value that only depends on the capture threshold b.
Maximum is reached for a certain optimal collision set size n*
Question: What’s the scaling behavior with more and more nodes that transmit at less and less rate?

## Slide 117: What is RFID

## Slide 118: What is RFID
RFID = Radio Frequency Identification
An RFID tag is an object that can be applied to or incorporated into a product, animal, or person for the purpose of identification using radiowaves
Some tags can be read from several meters away and beyond the line of sight of the reader
Wikipedia definition of RFID
Notes: From Wikipedia

## Slide 119: Components and types of RFID tag
Antenna: for receiving and transmitting the signal
Integrated Chip
Plastic Inlay
Maybe sensor, battery, external memory…
TYPES
Passive: no battery, the electrical current induced in the antenna by the incoming radio frequency signal provides just enough power in the tag to power up and transmit a response
Active: internal power source, which is used to power the integrated circuits and broadcast the signal to the reader
Semipassive: similar to active tags in that they have their own power source, but the battery only powers the microchip and does not broadcast a signal.
125/134 kHz
13,56 MHz
868/915 MHz
>2,4 GHz
international standard for RFID: Epc Gen2 Electronic Product Code Generation 2:
From Wikipedia

## Slide 120: Communication in passive tags
Reader transmits a wave signal
And transmit the answer to the reader
The tag’s antenna gets the power
This power is sufficient to read the data saved in the chip
Image from Alien Guide
Image from Alien Guide

## Slide 121: RFID vs BAR CODE
Is possible to attach a tag on many surfaces
No line-of-sight
Many informations and/or applications
Can be reprogrammed in the field to reflect current information
Cheap: 0,20 $
Now everything has a bar code
Requires line-of-sight
Only ID information
Data is fixed at the moment the label is printed
Cost free
RFID
BAR CODE
..but RFID are not only for identification scope..