## Slide 1: Signal processing: a networking perspective Part 1
Andrea Zanella
PhD Summer School of Information Engineering – 7-11 July, 2014 – Brixen (BZ)
zanella@dei.unipd.it
SIGnals processing & NETworking research group
SIGNET

## Slide 2: Outline
Part 1: introduction
  Who am I?
  Signal processing at network layer
  Where are we going?
  1st break
  What are the upcoming research challenges?
  Which are the main approaches?
  2nd break

## Slide 3: Outline
Part 2 – option A:
Signal processing at PHY/MAC layers
  Signals and signal processing from a network perspective
  The massive access challenge
    RFtag counting and identification
  Interference models & system capacity
    Multi-packet reception and Successive Interference Cancellation

## Slide 4: Outline
Part 2 – option B:
QoE-oriented networking
  Mixing up PHY and application-layer signals
    smart environments
  Context awareness from signal processing
    SSIM characterization of video content

## Slide 5: Let’s start with… my self-introduction!

## Slide 6: SIGNET people

## Slide 7: Main research areas…
Next generation mobile & IoT
Underwater communications
Cognitive Networks
Energy harvesting

## Slide 8: Plus more exotic stuff…

## Slide 9: Recent Research Projects
2010-2013: “IoTa” (sensor networks)
2010-2014: “SWAP” (sensor networks)
2010-2013: “Medieval” (cellular networks)
2010-2012: “SaPHYre” (cellular networks)
2010-2013: “CLAM” (underwater networks)
2010-2013: IIT – NAUTILUS (underwater networks)
2008-2010: “Aragorn” (cognitive networks)
2009-2010: “NEWCOM++” (ad hoc networks)
2007-2010: “SENSEI” (sensor networks)
2010-2014: EDA – RACUN (underwater networks)
2010-2012: ONR (underwater channel modeling)
2010-2011: JHU/APL (underwater MAC protocols)
2010-2011: VideoTec (wireless sensor networks)
2011-2012: Patavina Technologies (wireless sensor networks)
2009-2011: ARO@UCSD (cognitive networking)
2010-2013: NSF@UCSD (underwater localization and networking)
European
Others

## Slide 10: Collaborations
Qualcomm
NTT DoCoMo
Lucent Bell Labs
ST Microelectronics
NATO Undersea Research Centre
IBM Zurich research Lab
Ericsson Research
Telecom Italia Labs
Alcatel CIT
European Space Agency
Massachusetts Institute of Technology (MIT)
Stanford University
Univ. of South California (USC)
University of Illinois – Urbana Champaign
Univ. of California San Diego (UCSD)
Univ. of California Los Angeles (UCLA)
Inria – Sophia Antipolis (Francia)
Pennsylvania State University
New Jersey Institute of Technology
Centre Tecnològic de Telecomunicacions de Catalunya (CTTC – Barcellona)
German Airospace Center (DLR)
Scripps Institution of Oceanography (at UCSD)
Woods Hole Oceanographic Institution (Massachusetts)
National University of Singapore
Industrial
Academic

## Slide 11: Contacts
Leonardo Badia – badia@dei.unipd.it
Michele Rossi– rossi@dei.unipd.it
Andrea Zanella – zanella@dei.unipd.it
Michele Zorzi – zorzi@dei.unipd.it

## Slide 12: Signal processing…
from a networking perspective…
Image taken from: http://www.benheyman.com/lessons-for-better-networking-with-social-media/

## Slide 13: Signal processing from wikipedia perspective
Signal processing is an area of systems engineering, electrical engineering and applied mathematics that deals with operations on or analysis of analog as well as digitized signals, representing time-varying or spatially varying physical quantities. Signals of interest can include sound, electromagnetic radiation, images, and sensor readings, for example biological measurements such as electrocardiograms, control system
signals, telecommunication transmission signals,
and many others.

## Slide 14: Signal processing from IEEE prespective
"The Signal Processing Society's Field of Interest shall be the theory and application of filtering, coding, transmitting, estimating, detecting, analyzing, recognizing, synthesizing, recording, and reproducing signals by digital or analog devices or techniques. The term `signal' includes audio, video, speech, image, communication, geophysical, sonar, radar, medical, musical, and other signals."

## Slide 15: Signal processing from networking perspective?
http://www.mynamesnotmommy.com/yes-there-are-dumb-questions/question-mark/

## Slide 16: A tentative definition
From a networking perspective, signal processing refers to operations on or analysis of signals of diversified nature, representing time-varying or spatially varying physical quantities, but also functional processes

## Slide 17: Type of signals
Physical signals include
  Radio signals
    strength (RSS), angle of arrival, time of flight, phase…
  Environmental signals
    Temperature, humidity, CO2, pollution, acoustic noise,…
Functional processing signals include
  Application-related signals
    rate/distortion characteristic of videos, traffic patterns,…
  Protocols
    ARQ, RTS/CTS, probing, paging, signalling,…
  User’s profile-related “signals”
    Habits, app preferences, service preferences, mobility pattern…

## Slide 18: Question: what do we do with such signals
what do we do with such signals?
Question

## Slide 19: Depends on the perspective…
An (ipersimplified and totally biased) vision
  Physical layer perspective: more bitrate!
  Application layer perspective: more codecs!
  Network layers perspective: more performance!

## Slide 20: If communication services were hamburgers
Physical layer  bread
  Necessary to sustain all the rest
Application layer  sauce
  Different choices, different colors, different tastes, but not much substance
Network layers  meat
  what makes the difference between a sad BigMac
  and a rich, juicy, Jack-In-the-Box house burger!
http://latimesblogs.latimes.com/dailydish/2008/12/jack-in-the-box.html

## Slide 21: Where are we going to?
That is to say: what shall we expect from next generation of ICT?

## Slide 22: Your perspective!
What YOU expect from ICT’s next generation?

## Slide 23: Audience says…
IP TV
Assisted living
E-health
Self driving cars
Domotica
Holographics videocalls
Teletransport
Advanced 3D printers
Augmented reality
Ubiquitous connectivity
HD mobile video (with high QoE)
Longer device battery life
Energy harvesting devices

## Slide 24: Big players say…
No one actually knows…
but
there’s consensus on some points…

## Slide 25: Ubiquitous connectivity
Human users would like to be connected
  at all times
  regardless of their current location
  with good enough quality to enjoy the required service
European Union average
Italy, broadband penetration
21.9% (Jan 2011)
http://mapsengine.google.com

## Slide 26: Much more mobile traffic
Cisco Visual Networking Index: Global Mobile Data Traffic Forecast Update, 2013-2018, White Paper, Feb. 2014.
Mobile video traffic exceeded 50% for the first time in 2012, 53% in 2013 and counting…
Notes: Global mobile data traffic grew 70% in 2012 and 81% in 2013
Network operators requested to provide high-performance computing and delivering video traffic despite of the available resource

## Slide 27: Much more video traffic
www.futuretimeline.net/21stcentury/2020.htm
Ultra high definition
Holographic TV

## Slide 28: Full immersive experience
http://www.text100.com/hypertext/2013/04/homo-numericus/
3D reconstruction
obtained from a number of pictures captured from collaborating different viewpoints
[Microsoft Photosynth]

## Slide 29: Web evolution
Web 1.0: the world wide web
  Connects information
    easy access to data irrespective of their location
    Users are mainly data consumers
Web 2.0: the social web
  Connects people
    easy sharing of data
    Users are both data producers and consumers
Web 3.0: the sematic web
  Connects knowledge
    personalized data
    Geo-time tagged content, context-dependent web

## Slide 30: Web 4.0?
Web 4.0: symbiotic web
  Strict interaction among humans and machines
  According to Daniel Burrus, Web 4.0 is about
  “the ultra-intelligent electronic agent”
    It will recognize you when you get in front of it
    It will know your habits and act accordingly
    It will debate with you if you deviate from the right way…
  Mmmmhhh… sounds like a movie’s plot…
By the way… if you’re wondering who is Burrus, well he is a futurist and business strategist… Check it out here: http://www.burrus.com

## Slide 31: Internet of Things

## Slide 32: The Internet (of Things)

## Slide 33: Motivation
What
  Providing Internet connection to potentially ANYTHING
When
  ~1995  WSN
  ~2000  IoT
  ~2020  hundred of BILLIONS of devices connected
Why
  A (still largely unforeseen) plethora of new services
    Smart Cities, Smart Grids, Smart everything!
  huge, Huge, HUGE market (again… potentially)

## Slide 34: The Business Perspective
Cisco
  The estimated market of $14.4 Trillion up for grabs in the coming decade
Intel
  IoT brought about $2 billion of the company's $12.8 billion in revenue, which equated to 32% growth year over year
IBM
  Since 2003 IBM spent over $50 billion on acquisitions and R&D in preparation for a radical shift in IBM's business

## Slide 35: Enabling technologies
Wireless Sensor Networks
Wired
connections
Powerline Communication
Cellular
WiFi
RFID

## Slide 36: IoT

## Slide 37: Number of interconnected objects
  Jim Morrish, Principal Analyst at Analysys Mason http://www.analysysmason.com/About-Us/News/Press-releases/Internet-of-Things-will-grow-to-16-billion-connectable-consumer-devices-by-2020-says-Analysys-Mason/
  Steve Hilton, Principal Analyst at Analysys Mason http://www.analysysmason.com/Research/Content/Reports/RRE02_M2M_devices_forecast/
Chart: 
| Sensori | M2M
Oggi | 120 | 62
2020 | 16000 | 2000
[Millions]
Today
Today
Sensors

## Slide 38: What’s a machine
Any device (or software) that can perform automated tasks, e.g., smartphones, refrigerator, sensors, etc.
Devices that can
  take autonomous decisions based on information received from other devices
  in a mostly unsupervised manner
  act much smarter than traditional devices

## Slide 39: Example: assisted living
Remote monitoring of health status

## Slide 40: Example: assisted living
Remote monitoring of health status
Remote assistance

## Slide 41: Example: assisted living
Remote monitoring of health status
Remote assistance
Automatic first aid request

## Slide 42: Example: assisted living
Remote monitoring of health status
Remote assistance
Automatic first aid request

## Slide 43: Indoor navigation

## Slide 44: Self-sustainable forest fire detection system

## Slide 45: Smart ambient
ID=1, Laptop
ID=2, cellphone
ID=3, ashtray
ID=4, keys
ID=5, Tablet PC
Who’s out there?
ID | Object type
3 | ashtray
5 | Tablet PC
4 | Keys
1 | Laptop
2 | Cell phone
Smart Objects Lists

## Slide 46: Workplace comfort & health
Indoor environments
  CO2 < 600 ppm
  CO2 >1000 ppm
  CO2 >2500 ppm
Experimental study: scuola media Coletti Feb/2009
  CO2 level
    after 30 min  1950 ppm
    opening the window for 5 min  800 ppm
    outdoor  600 ppm

## Slide 47: VANET: Vehicular networks
Vehicles Transformed into “Computers on the Wheels” or “Networks on the Wheel”
Vehicular Communication System (VCS):
  Vehicle to Vehicle (V2V) Communication
  Vehicle to Infrastructure (V2I) communication
Advantage and Usage of VCS:
  Information sharing
  Co-operative driving
  Other value added services like Navigation, internet access etc.

## Slide 48: VANET services
Propagation of emergency and alert messages
  Uses multi-hop/multi-cast technique
  Intelligent broadcasting
High bandwidth link with vehicle and roadside equipment
  Entertainment
  Internet access
Multi hop unicast, Geocasting, Mobicasting
  Gaming
  Messaging
  Platooning
  …

## Slide 49: Smart Cities
“Smart City” is all about applying ICT in operating the public affairs
  make a better use of the public resources
  Increase quality of life in the urban areas
  reduce the operational costs of the public administrations
  Reduce the gap between citizens and administrations
One concept, several flavors
  Smart Governance, Smart Mobility, Smart Utilities, Smart Buildings, and Smart Environment

## Slide 50: Smart City: example of services
For the administrations
  Monitoring of traffic
    Real-time monitoring of city viability, help assessing impact of traffic plans, plan public events,…
  Monitoring of public transportation
    Timing, utilization, peak hours…
  Monitoring of public facilities
    Street lights, bike sharing, car sharing, trash bins, gym facilities in parks,…
  Monitoring of pollution, noise level, maintenance teams,…
For the citizens
  Better services
  Easier interaction with administrations
  More transparency in municipality economical plans

## Slide 51: Smart Grid
Household energy usage accounts for ~50% electric & ~33% energy usage in Italy
  Extremely important to improve building energy efficiency
In 2005 ENEL starts deploying the first SMART GRID
  Cost: 2.1 billion euros
  Saving: 500 milions per year!
USA: Energy Dep. forsee up to 117 billions of dollars saving by 2030
Smart grid can also decrease CO2 emission of 12% in USA & 15% in India
Fonti: *Ministero dello Sviluppo Economico, 2005
  National Energy Technology Laboratory (2007-08) (PDF). NETL Modern Grid Initiative — Powering Our 21st-Century Economy. United States Department of Energy Office of Electricity Delivery and Energy Reliability. p. 17. Retrieved 2008-12-0
  R.G. Pratt, M.C.W. Kintner-Meyer, P.J. Balducci, T.F. Sanquist, C. Gerkensmeyer, K.P. Schneider, S. Katipamula, T.J. Secrest. The Smart Grid: An Estimation of the Energy and CO2 Benefits. Pacific Northwest National Laboratory Prepared for the U.S. Department of Energy under Contract DE-AC05-76RL01830
  Molly Webb, McKinsey & Company. SMART 2020: Enabling the low carbon economy in the information age. A report by The Climate Group on behalf of the Global eSustainability Initiative (GeSI)

## Slide 52: Summing up, ICT shall provide…
infinite capacity
  Everyone gets what needed to be happy!
ubiquitous coverage
  No more connectivity gaps!
pervasive connectivity
  “Every” object is Internet-enabled
customization
  Services adapt to the context and the personal requirements
flexibility
  Easy development and integration of new services

## Slide 53: First Break
We deserve it!
http://www.keepcalmstudio.com/gallery/poster/L90JKS

## Slide 54: Technological challenges

## Slide 55: Your perspective!
What YOU expect is needed to realize these goals?

## Slide 56: Big players say…
No one actually knows…
but
there’s consensus on some points…

## Slide 57: Technical requirements
Infinite capacity
  Everyone gets what needed to be happy!
More rate
More spectrum efficiency
More spatial reuse
QoE-based RRM
Dynamic content caching
…
User asks for
Engineer understands…

## Slide 58: Technical requirements
ubiquitous coverage
  No more connectivity gaps!
multiple RATs
new frequency bands
multiple antennae & beam forming
cell densification
higher sensitivity
better handover
…
User asks for
Engineer understands…

## Slide 59: Technical requirements
pervasive connectivity
  “Every” object is Internet-enabled
protocols protocols protocols!
  6LowPAN, RPL, CoAP,…
massive access management
energy efficiency
security
…
Engineer understands…
User asks for

## Slide 60: Technical requirements
customization
  Services adapt to the context and the personal requirements
software adaptability
quality of experience
service differentiation
context awareness
  Machine learning
  Unsupervised learning
  Emergent behavior, …
User asks for
Engineer understands…

## Slide 61: Technical requirements
flexibility
  Easy development and integration of new services
semantic web
  Ontologies
data accessibility
heterogeneous sources
  wideband services (voice, video, web,…)
  machine-type devices
  Highly mobile users (VANET, trains,…)
User asks for
Engineer understands…

## Slide 62: And much much more…
Protocol transparency
Routing
Data storage
Ranking
Connectivity
Service-enablement
Mobility
Heterogeneity
Deployability
Manageability
…
Scalability
Real-time processing
Tracking/positioning
Application development
Access
Human-things interaction models and paradigms
Service/Device discovery
Security, access control, sharing of physical things on the Web
…

## Slide 63: Let’s try to quantify
Massive capacity and massive connectivity (104 – 105 per BS)
1000 times higher mobile data volume per unit area
10-100 times higher # of connecting devices & user rate
  e.g., peak data rate of 10 Gbps for low mobility and peak data rate of 1 Gbps for high mobility
Less than 1 ms latency to support real-time control applications
Max 10 ms switching time between different radio access technologies (RATs)
Communication scenarios in the range of 350 - 500 km/h
  compared to 250 km/h in 4G networks
10 times longer battery life

## Slide 64: The way forward…
Maybe…

## Slide 65: Your perspective!
What YOU expect is the way to achieve these goals?

## Slide 66: Big players say…
No one actually knows…
but
there’s consensus on some points…

## Slide 67: The basic ingredients
Next generation of ICT
Advanced PHY
Cognition & machine learning
HetNets & multi-RAN
Software defined networks
Native MTD support

## Slide 68: Advanced PHY
Massive MIMO
Mm-wave communication
Full duplex communication
…

## Slide 69: Advanced PHY: more bitrate
Formula for Network Throughput:
Ways to achieve 1000x improvement
  Throughput =Available spectrum ∙ Cell density ∙ Spectral efficiency
bit/s in area
Hz
Cells/area
bit/s/cell/Hz
http://wireless.kth.se/wp-content/uploads/2014/03/presentation_massiveMIMOmagic.pdf

## Slide 70: Massive MIMO
Massive MIMO usea large arrays at BSs
  e.g., 𝑁≈200 antennas, 𝐾≈40 users
Key: Excessive number of antennas, 𝑁≫𝐾
Very narrow beamforming
Little interference leakage

## Slide 71: Advanced PHY: more spectrum
New frequency bands
  mm-wave communications (>60 GHz)
  5 – 9 GHz of unlicensed bandwidth
  Ever heard of WiGig (IEEE 802.11ad)?
    http://www.wi-fi.org/discover-wi-fi/wigig-certified

## Slide 72: mmWave advantages
http://www.slideshare.net/allabout4g/intel-25905453

## Slide 73: Advanced PHY: Full duplex
Full duplex wireless transmission
  Passive and active cancellation of interfering transmitted signal
  Potentially capable of doubling capacity with same RF resources
  Need careful design of MAC as well…

## Slide 74: The basic ingredients
Next generation of ICT
Advanced PHY
Cognition & machine learning
HetNets & multi-RAN
Software defined networks
Native MTD support

## Slide 75: Native support for Machine-type communication (MTC)
Exploit correlation of sensor data across space and time
  better scalability if properly used
Radically new frame structure
  highly reliable connections despite coverage problems
  Reduce signaling
  More on this in Part 2…
Exploit X-layer solutions
  Spreading codes plus successive interference cancellation
  More on this in Part 2…

## Slide 76: The basic ingredients
Next generation of ICT
Advanced PHY
Cognition & machine learning
HetNets & multi-RAN
Software defined networks
Native MTD support

## Slide 77: HetNets & multi-RAN
Heterogeneous networks (HetNets):
  Small cell networks including macrocells and small cells of all types
  Provide improved spectrum efficiency (bps/Hz/km2), capacity, and coverage
  Small cells can support wireless applications for homes and enterprises as well as metropolitan and rural public spaces
  Require solutions for cell selection, handover, dynamic content caching, …

## Slide 78: The basic ingredients
Next generation of ICT
Advanced PHY
Cognition & machine learning
HetNets & multi-RAN
Software defined networks
Native MTD support

## Slide 79: Planes of Networking (1/2)
Data Plane
  All activities involving as well as resulting from data packets sent by the end user, e.g.,
    Forwarding
    Fragmentation and reassembly
    Replication for multicasting
Control Plane
  All activities that are necessary to perform data plane activities but do not involve end-user data packets
    Making routing tables
    Setting packet handling policies (e.g., security)
    Base station beacons announcing availability of services
Ref: Open Data Center Alliance Usage Model: Software Defined Networking Rev 1.0,”
http://www.opendatacenteralliance.org/docs/Software_Defined_Networking_Master_Usage_Model_Rev1.0.pdf

## Slide 80: Data vs control planes
Data plane runs at line rate
  e.g., 100 Gbps for 100 Gbps Ethernet  Fast Path
  Typically implemented using special hardware
  Few activities handled by CPU in switch  Slow path
    e.g., Broadcast, Unknown, and Multicast (BUM) traffic
All control activities are generally handled by CPU

## Slide 81: OpenFlow key idea
Separation of control and data planes
Centralization of control
Flow based control
  Control logic is moved to a controller
  Switches only have forwarding elements
  One expensive controller with a lot of cheap switches
  OpenFlow is the protocol to send/receive forwarding rules from controller to switches
Ref: N. McKeown, et al., ``OpenFlow: Enabling Innovation in Campus Networks," ACM SIGCOMM CCR, Vol. 38, No. 2, April 2008, pp. 69-74.

## Slide 82: OpenFlow basics
On packet arrives to the switch
Switch logic compares header fields with flow entries in a table
  if any entry matches  perform indicated actions
  If no header match 
    packet is queued and header is sent to the controller
    Controller sends a new rule to the switch
    subsequent packets of the flow are handled by this rule
Doesn’t all of this remind you anything?
Ref: N. McKeown, et al., ``OpenFlow: Enabling Innovation in Campus Networks," ACM SIGCOMM CCR, Vol. 38, No. 2, April 2008, pp. 69-74.

## Slide 83: What do we need SDN for?
Virtualization: Use network resource without worrying about where it is physically located, how much it is, how it is organized, etc.
Orchestration: Manage thousands of devices
Programmable: Should be able to change behavior on the fly
Dynamic Scaling: Should be able to change size, quantity
Automation: Lower OpEx
Visibility: Monitor resources, connectivity
Performance: Optimize network device utilization
Multi-tenancy: Sharing expensive infrastructure
Service Integration
Openness: Full choice of Modular plug-ins
Unified management of computing, networking, and storage
http://www.cse.wustl.edu/~jain/tutorials/icc14.htm

## Slide 84: Network Function Virtualization (NFV)
Fast standard hardware  Software based Devices Routers, Firewalls, Broadband Remote Access Server (BRAS)  A.k.a. white box implementation
Function Modules (Both data plane and control plane)  DHCP (Dynamic Host control Protocol), NAT (Network Address Translation), Rate Limiting
Ref: ETSI, “NFV – Update White Paper,” Oct 2013, http://www.tid.es/es/Documents/NFV_White_PaperV2.pdf (Must read)

## Slide 85: Overall “software-defined” summary
OpenFlow separates control plane and moves it to a central controller
  Simplifies the forwarding element
SDN is the framework to automatically manage and control a large number of multi-tenant network devices and services
  OpenFlow originated SDN but now many different southbound and northbound APIs, intermediate services and tools are being discussed and implemented by the industry
OpenDaylight SDN Controller platform is the leading open source SDN controller project under Linux Foundation
NFV reduces OpEx by automation and scalability provided by implementing network functions as virtual appliances
http://www.cse.wustl.edu/~jain/tutorials/icc14.htm

## Slide 86: The basic ingredients
Next generation of ICT
Advanced PHY
Cognition & machine learning
HetNets & multi-RAN
Software defined networks
Native MTD support

## Slide 87: The cognition cycle
Sense
Learn
Act

## Slide 88: True for human, true for networks
Sense: nowadays devices are crammed with transducers/sensing apparatuses
  needs efficient data handling
Learn: optimization algorithms can be run at each node individually
  needs (i) efficient algos (ii) harmonization
Act: network modifies the environment
  requires convergence of multiple devices

## Slide 89: Supervised vs unsupervised learning
Supervised learning requires a training set and/or instructions of good/bad
  Better for limited improvements in well known scenarios
Unsupervised has no prior knowledge
  No pre-existing (arbitrary) model
  Just emerging behavior
  and distributed optimization

## Slide 90: Cognition-based Network
Each node of the network:
  exploits local information to achieve its goal
  shares it with its neighbors
Self-adaptation to the environment to achieve network wide goals
Cognition applied to the entire network (more on this on Part 2 – option B)

## Slide 91: Conclusions of Part 1 (1/3)
Big expectations for next generation ICT
  “Infinite” capacity & “zero” delay
  Full coverage & pervasive connectivity
  Energy efficiency & self sustainable systems
  New services and applications

## Slide 92: Conclusions of Part 1 (2/3)
A lot of open problems
  Massive access
  Extremely heterogeneous traffic patterns
  Higher and higher user mobility
  Increased traffic demand
  Increased QoE expectation
  Self adaptability and “smart” behavior
  …

## Slide 93: Conclusions of Part 1 (3/3)
A lot of possible solutions
  New PHY: e.g., massive MIMO, mmwave, full duplex,…
  Clean-slate design of control plane: native support for MTC & wideband services
  HetNets: cell densification, multi-RAN, multi-hop, cooperative transmissions,…
  Software-defined: SDN, NFV, Cloud
  Cognitive approach: instill intelligence into network elements

## Slide 94: Break!!!! We all need it!
http://www.overstock.com/Home-Garden/Keep-Calm-and-Drink-Coffee-Unframed-Print/7967447/product.html

## Slide 95: Spare slides

## Slide 96: IoT: sw&hw
Protocols and interfaces
  Theory, Simulation, Implementation
  Highly scalable
  Easy data access
  Robustness and security
Performance optimization
  Low energy consumption
  Energy harvesting
  Real time features
  Data redundancy and consistency
Optimization of the hardware and software
  Lower devices cost
  Lower maintenance costs

## Slide 97: IoT: modelling and analysis
Accurate models for environment and physical processes
  Estimate and prediction of the monitored processes
  Minimization of data exchange
    Lower interferences
    Lower power consumption

## Slide 98: Net generation mobile

## Slide 99: 5G networks and services
What
  4th generation: LTE-Advanced, based on OFDMA
  Wireless LANs and emerging .11 standards
  Multimedia: adaptive and scalable contents
When
  LTE-A started being deployed end of 2012
  Video has been the majority of traffic since 2012
Why
  Many resources (peak rates of 1Gb/s) but even higher requirements due to several users

## Slide 100: Example: emergency scenarios
Forest fires: 50k/year in Europe
Road accidents: 2M/year in Europe with 100k deaths and 3.5M injured
Earthquakes, tsunamis, terrorist strikes
Problems: Unreliable infrastructure, rescuers are not coordinated
Challenges: Avoid network collapse, replace destroyed networks, keep enabling rescue communications

## Slide 101: Research topics
Resource allocation strategies for LTE
Handover strategies
Adaptation and optimization

## Slide 102: Underwater communications
1
Sink
3
4
5
6
7
CO2
CO2
2
Increased traffic rate
~200 m
~400 m
~1000 m
~100 m
~200 m

## Slide 103: Underwater communications
What
  Acoustic communications instead of radio
When
  Sonar technologies have been used since 1930s
  21st century technologies: higher bandwidth/rate
Why
  Oceanography/security/monitoring applications
  The channel is extremely difficult to characterize
  Infrastructure monitoring is critical (oil pipes)
  Networking under development
Notes: What
  Acoustic communications instead of radio
When
  Sonar technologies have been used since 1930s.
  21st century technologies: higher bandwidth/rate
Why
  Oceanography/security/monitoring applications
  The channel is extremely difficult to characterize
  Infrastructure monitoring is critical (oil pipes)
  Networking under development

## Slide 104: Example
Application funded by US NAVY
Endurance test: keep the submarine under!
  Rather than emerging to communicate, stay underwater and make use of a relay network of seabed anchored repeaters
  Saving in the order of milions of $$$!

## Slide 105: Research topics
Protocol design
  MAC, Routing, Error control
Channel characterization
  Correlation, impact on protocols
  Real data sets
Performance analysis
Experiments and sea trials

## Slide 106: Cognitive networks
Image taken from
http://www.cosolen.com/syntactic-variation-in-cognition/
Notes: Il filone di ricerca delle cognitive networks mira a riprodurre I processi di apprendimento e decisione tipici della persona umana in un contesto di reti di telecomunicazioni, in modo da sviluppare algoritmi e protocolli che permettano agli elementi di una reti di osservare il contesto in cui operano, apprendere l’effetto delle proprie azioni sul contesto, e quindi imparare autonomamente la strategia migliore da adottare in base al contesto.

## Slide 107: Cognition-based networks
What
  Heterogeneous access technologies…
    WiFi, LTE, Ethernet, ZigBee,...
  and traffic: video, voice, sensorial/tracking data..
When
  Relevant standards 802.21-22 released 2009-11
  MIMO in next LTE-A, IEEE 802.11ac (exp 2014)
Why
  Complicated X-layer optimization
  Context awareness and adaptability
  Exploitation of known patterns
Notes: Queste tecniche dovrebbero permettere una gestione efficiente delle reti, la cui complessità è andata crescendo esponenzialmente negli ultimi anni grazie all’introduzione di tecnologie nuove e articolate, come WiFi per le reti locali, LTE per le reti cellulari, ZigBee per le reti domestiche e di sensori, e alla sempre maggior varietà dei flussi dati da trasportare. As esempio, lo standard 802.11 su cui si basa WiFi, è stato oggetto di una continua evoluzione ancora in corso, con aggiunta di elementi sempre nuovi e più complessi, come il supporto della QoS, la possibilità di scambiare informazioni di contesto tra AP, e l’introduzione di antenne multiple per MIMO prevista nel 2014.

## Slide 108: Example: video via WiFi
No congestion, close to AP  smooth, HD video 
Suddenly, video starts freezing: why?
  user moving away from the AP  poor RF signal
  Internet connection is congested  poor ADSL
  other users are watching videos  poor scheduling
Countermeasures are different:
  switch to APs with better signal, use collaborative techniques, change video codec,…
  tune RTP parameters, change video codec,…
  cache video content at AP, implement VAC, switch to multicast…
How to choose? Cognitive techniques!

## Slide 109: Research topics
Context classification techniques
  Infer congestions, channel conditions, traffic types, in-network delays,…
Convergence to global optimal behavior
  Apply emergent behavior techniques to find optimal parameters setting in a distributed fashion
Network optimization
  Learn optimal actions by means of neural networks

## Slide 110: HetNets: cell sizes
Femtocell
  small area covered by a femto access point (FAP), intended for residential indoor applications, installed and managed by the customers
  Key attributes: IP backhaul, self-optimization, low power consumption, ease of deployment (user-deployed), closed/open/hybrid access
Picocell
  low-power compact base stations, used in enterprise or public indoor areas, encompasses outdoor small cells as well
  Key attributes: wired or wireless backhaul, operator deployed, self-optimization, open access
Microcell
  outdoor short-range base station aiming at enhancing coverage for both indoor and outdoor users
  Key attributes: wired or wireless backhaul, self-optimization, low power consumption, open access
Metrocell
  small cell technologies designed for high-capacity metropolitan areas, typically installed on building walls, lampposts; can include technologies such as femtocells, picocells, and microcells
  Key attributes: wired or wireless backhaul, operator deployed, self-optimization, open access
Relays: operator deployed, open access, wireless backhaul

## Slide 111: Planes of networking (2/2)
Management Plane
  All activities related to provisioning and monitoring of the networks
    Fault, Configuration, Accounting, Performance and Security (FCAPS)
    Instantiate new devices and protocols (Turn devices on/off)
    Optional  May be handled manually for small networks
Services Plane
  Middlebox services to improve performance or security, e.g.,
    Load Balancers, Proxy Service, Intrusion Detection, Firewalls, SSL Off-loaders
    Optional  Not required for small networks