## Slide 1: TCP Performance Enhancements in Wireless Mesh Networks, problems, ongoing work and future
  Presenter:
  Jonas Karlsson
  Karlstad University
  jonas.karlsson@kau.se
Newcom++ Summer School - Bressanone Italy – 2 July 2008

## Slide 2
Wireless Mesh Networks
Wireless mesh networks (community style)
  Fixed wireless backbone, nodes can turn on/off
  Mobile clients
  1 or more gateways to connect to the Internet
Wireless Mesh Network
Internet
GW

## Slide 3: Overview WMN’s
Pros:
  Nodes can be ”expensive”
    more than 1 radio, mimo , medium size antennas etc.
  ”Unlimited” power/energy
  No mobility 
  Setup time is not crucial (minutes)
  Medium size (community)
Cons:
  Users expect same performance as wired internet connection (10/24/100 Mbit/s)
  Self-configuration (community)
  Off the Shelf hardware, mainly means phy and mac layer are “untouchables”
  The most widely used protocol on Internet (TCP) is not working very well in multi-hop scenarios

## Slide 4: Overview Research
Area
  ”Useable” Wireless Mesh Networks
    Performance
      TCP performance/robustness
    Ease of Use/Deployment (Auto-configuration)
Open Topics/Problems
  Today's performance is not adequate for general use
    TCP causes severe contention of the wireless medium.
  Configuration/installation of the network is inflexible/static
    To form a network requires ”hands on” + special programs
    The ”network” should be self-aware and adapt to changing conditions

## Slide 5: Ongoing work and future
Too many packets cause contention (ongoing)
  Packet aggregation (ns 2 and Linux implementation)
  TCP window scaling/limit (auto-configured)
  TCP MSS adjustment (packet loss causes retransmissions)
Intra/inter flow interference (future)
  Is the problem really in the transport layer?
    Is it worth optimizing 10-40% at transport layer when 50% are already dropped at MAC
  Reduce data and ack collision, network coding?
  Multi-channel/radio network deployment
  Transmission powercontrol
What is cause, what is effect and where to solve?

## Slide 6: Packet Aggregation
To fully exploit the available bandwidth
  aggregation needs to be adaptive to changing channel conditions
  In a multi-hop scenario this must be done on a hop-by-hop basis

## Slide 7: Results